## Slide 1
LINK
GROUP
LINK
GROUP
Automation Engineering (Shanghai) Co.,Ltd.
Training Record
Pham Tung Lam : PLC Engineer
Module Safety
霖和自动化工程(上海)有限公司

## Slide 2
The safety program is called up cyclically and is therefore synchronous to the standard program . The F-runtime group is processed before the standard program. → The number of the standard OB is greater than the F-runtime group OB
This increases the protection against manipulation from the standard program
SAFE CONCEPT GSC

## Slide 3
In the GSC zone concept, the safe actuators are switched off regardless of the call structure in the safety program.
In the main FFB all stations called one after the other.

## Slide 4
The zone used is configured in each component in the various stations.
ST020 tool and ST040 conveyor technology each use E-STOP circle 1
ST020 tool uses SAFETY GATE circuit 2 ST040 conveyor technology uses SAFETY GATE circuit 4

## Slide 5
OVERVIEW | SAFE STRUCTURE

## Slide 6
In the F-program, the system programmer has the following options
1-32 emergency stop zones
1-32 gate zones (protective circuit zones)
Each safety device need to be assigned a zone and estop zone number

## Slide 7
_ All safe actuators contain the following saving releases
_ The emergency stop and protective circuit releases are canceled or acknowledged by the zone configured on the actuator.
_ The MISC release is available at the actuators (as far as provided by the standard) as a discrete input at the failsafe modules of the actuators.
_ The "MISC" input can be used to implement other safe deactivations that cannot be implemented with the zone concept.
_ By default, discrete deactivations of individual or a small number of actuators are implemented in the GSC (operator's loading station).

## Slide 9
LINK Group Headquarter
Shanghai, China
Contact Us
Enquiry
ying.liu@LKautomation.com
+86 021 6918 0161
Sales
gene.zhang@LKautomation.com
+86 136 2179 1621
Address
BLDG #D,North Jiasong Road No.3570 Jiading District,Shanghai,P.R.China
LINK Group North China
Shenyang, China
LINK Group Europe (LKGG GmbH)
Bad Reichenhall, Germany
Enquiry
kimi.wang@LKautomation.com
+86 021 6918 0161
Sales
gene.zhang@LKautomation.com
+86 136 2179 1621
Address
NO. 14 22nd Floor,NO.168-3 Harbin Road,
Shenhe District,Shenyang,Liaoning
Province,P.R.China
Enquiry
jackey.yin@LKautomation.com
+86 186 2171 9367
Sales
andreas.reymendt@LKautomation.com
Address
Fischerbraeuwiese 18b,83435 Bad
Reichenhall,Bavaria,Germany