## Slide 1
LINK
GROUP
LINK
GROUP
霖和自动化工程(上海)有限公司
Automation Engineering (Shanghai) Co.,Ltd.
Staff name: Nguyễn Tuấn Phong ( Assistant PLC Engineer)
Mainly training: SOFTWARE STRUCTURE
General information
Structure
Operating Modes
Programming Specification
Training Record

## Slide 2
LINK
GROUP
General information
For support, the GSC standard offers its own help,
where we can find information on blocks, the
software structure and other standard
specifications.
We can find the help in the project directory under:
…\ UserFiles \ UserDocumentation \en-US.

## Slide 3
Or we can go into the program, select a block, press Shift + F1 to find instructions related to that block.
General information

## Slide 4
Structure
program
++ STxx / ++ FTxx
20 users
40 Obs_MAIN
99 GSC Common
data types
20 USER
20 User Type PLC
99 GSC Type PLC
30 safe
99 GSC list
99 GSC Type PLC
One folder per ST or FT
User blocks
All security components
All OBs
GSC data blocks
GSC message lists DBs
GSC program module
User-defined PLC data types
User-defined typed PLC data types
GSC typed PLC data types

## Slide 5
Each different station or FT has a Main_Block (for example: ST010_FB). Main block will call component blocks such as FX1, FX2, IR, OP, SD,.....
Main_OB is the component block that contains the functional blocks of each station
Structure

## Slide 6
So there is the superimposed station ++ST000. Disturbances at this level affect the overall operating mode of the PLC. Faults in lower levels, such as in the ++ST010, only affect the operating mode area of the ++ST010.
The concept of fault inheritance is also reflected for the selection of the areas on
the HMI for manual operation
ST000 is called the main structure including blocks such as: Media(Diagnosis of component devices), Mess(Notifications during operation and errors), OC(Main Panel of ST000), Safe, Type,. ....
Structure
Different from the Sicar standard with fixtures or multi-sequence actuators, we will have 3 function blocks: FX0xx_FB (Main start), SEQxx_FB(automatic graph), RESEQxx_FB(Home position), with a complex structure using Functional blocks help the structure continue the cycle without needing to return to the beginning when there is a problem such as power outage, E-stop,...

## Slide 7
DATA BLOCKS
Structure
building block | Theme | Description
MDS | MODE data | operating mode information
SDB / FSDB | SEQ data: | Connect standard blocks to graphs or related blocks
IDB / FIDB | INSTANCE data | instance data
UDB / FUDB | user data | Disallowed or temporary variables need to be used as initialization markers in the UDB

## Slide 8
Structure
As mentioned in the report on the TKB program, system levels such as LINE, PLC, SG, FG
Each ++ST0xx station is onegroup! An FG does notassigned to a groupautomatically through softwarestructure, but through clearlytasks in the programcode
We have the PLC level corresponding to ST000. All changes will be notified to Main_Sys_FB
GROUPINGOFCOMPONENTS

## Slide 9
Operating Modes
There are components WITH and WITHOUT operating modes. There are no operating mode ranges .
component | Reference AKZ_ | own operating mode | remark
Tool | FX001 TR001.FX001 | Yes | _
robot | IR001 | Yes | _
protective grille door | ++ST010+SD001 | no | _
worker place | ++ST010+WP001 | Yes | _
Each component with an operating mode has its own DB (MDB) for managing its specific data.
The MODE substructure manages all data relevant to the subject of operating modes .
IN / OUT area :
Is intended for the communication of the component to its subordinate blocks.
The communication is intended exclusively for standard blocks .
ONLY the OUT area may also be read in the user program

## Slide 10
Operating Modes
In block ST010+FX001_MDB
Each component with an operating mode has its own DB (MDB) for managing its specific data.
The MODE substructure manages all data relevant to the subject of operating modes .

## Slide 11
The operating mode DB (MDB) is initially configured at the component block level and then propagated to the individual internally called blocks:
The parameter #MDB is set up as a hidden parameter on all blocks that necessitate it: MODE, DEV, SENS, etc.
Operating Modes

## Slide 12
Main_OB
++ ST000_FB
MODE_PLC_FB
++ ST010_FB
PLC_MDB
++ST010_MDB
MODE_FG_GROUP_FB
++ ST010+IR001_FB
MODE_FG_FB
++ST010+IR001_MDB
MODE_FG_TO_GROUP_FB
...
++
ST010+TR001_FB
MODE_FG_FB
MODE_FG_TO_GROUP_FB
++ST010+TR001_MDB
HANDLING OF THE OPERATING MODES
Operating Modes
When Main_OB calls the ST010_FB block, it will check the mode of the devices currently in the MDB block, each device will respond the mode to its own MDB.

## Slide 13
Programming
Operating Modes
For each Panel we need to determine the IP address based on Eplan and the corresponding PN_DEV_NAME to be able to accurately diagnose profinet.For CONF_OP_RELEASE, 1 OP can only manage 1 ST. If you want that panel to control other signals, you need to change the level to ST000.

## Slide 14
LINK Group Headquarter
Shanghai, China
Contact Us
Enquiry
ying.liu@LKautomation.com
+86 021 6918 0161
Sales
gene.zhang@LKautomation.com
+86 136 2179 1621
Address
BLDG #D,North Jiasong Road No.3570 Jiading District,Shanghai,P.R.China
LINK Group North China
Shenyang, China
LINK Group Europe (LKGG GmbH)
Bad Reichenhall, Germany
Enquiry
kimi.wang@LKautomation.com
+86 021 6918 0161
Sales
gene.zhang@LKautomation.com
+86 136 2179 1621
Address
NO. 14 22nd Floor,NO.168-3 Harbin Road,
Shenhe District,Shenyang,Liaoning
Province,P.R.China
Enquiry
jackey.yin@LKautomation.com
+86 186 2171 9367
Sales
andreas.reymendt@LKautomation.com
Address
Fischerbraeuwiese 18b,83435 Bad
Reichenhall,Bavaria,Germany